This document was produced by Queensland mining-industry-based electrical personnel as a tool to assist mines protect their sites from lightning. While significant issues are raised, this document does not purport to cover all lightning-related hazards or available controls. It was published in its present form to be adapted or built upon by mines wishing to audit their status in addressing lightning-related hazards.

Lightning Protection Audit Tool for Mines

MINE:	AUDITOR/S:

DATE:	MINE REP: (Person/s involved during audit)

## Ref doc

| NO. | AUDIT ITEM | STATUS | COMMENTS |
| --- | --- | --- | --- |
|  | Have you identified lightning as a hazard on site? |  |  |
|  | If so, what controls do you have in place for each lightning hazard? |  |  |
|  | Do you use a lightning detection warning system? If so what system? e.g. http://www.lightning.net.au/klass.htm or www.weatherzone.com.au How does this system provide early warnings? |  |  |
|  | Conveyors/structures steel cored belt |  |  |
|  | How do you manage the risk of transferring lightning energy into the underground via the conveyor structure? What is the resistivity/metre for your steel cored belt? Do the stockpile conveyor and the trunk conveyor entering the mine have electrical continuity? Do the stock pile conveyor and the trunk conveyor entering the mine share foundations? Is the conveyor system covered by a metallic roof structure? Is there a lightning protection system (LPS) protecting the length of the conveyor? At what intervals is the structure connected to the general mass of earth by electrical conductors (earth electrodes)? At what intervals is the structure connected to the general body of earth via foundations? Is the Trunk conveyor structure entering the mine bolted together or pinned? What is the conductivity/per structure bay? What is the conductivity of the total length of the conveyor? Is the conveyor supported by chain via roof bolts? What is the resistance to earth from the conveyor structure to earth via the suspension chains and roof bolts? Is the conveyor structure electrically connected to the mine earth grid? |  |  |
|  | Services water/air/cables |  |  |
|  | How do you manage the risk of transferring lightning energy into the underground via the services? What is the resistivity/metre for your steel pipe? Is there an LPS protecting the length of the surface pipe work? At what intervals is the pipe work connected to the general mass of earth by electrical conductors (earth electrodes)? At what intervals is the pipe work connected to the general body of earth via foundations? Is the rubber joining ring of Victaulic pipe conductive? What is the resistance/per length of Victaulic pipe? What is the resistance of the total length of the Victaulic pipe? Is the Victaulic pipe supported by chain brackets via roof bolts? What is the resistance to earth from the Victaulic pipe to earth via the suspension chains and roof bolts? Is the Victaulic pipe electrically connected to the HV earth grid? |  |  |
|  | Drift lining materials |  |  |
|  | What percentage of the metallic drift lining is covered with earth? Is the metallic drift lining electrically connected to the general mass of earth (earth mat/electrode)? Is there a metallic annex cover over the drift entrance? Is the annex bonded to the metallic drift lining entrance? Is the lining/annex connected to the mine earth grid? Is the lining/annex connected via foundations? Is there an LPS to protect the drift lining/annex? |  |  |
|  | Rail systems |  |  |
|  | Is the rail track connected to the general mass of earth? Is the rail track laid on blue metal stone? Is the rail track joined to mine earth grid? Is there an LPS protecting the surface section of rail track? |  |  |
|  | Rope and winder systems |  |  |
|  | Are the ropes effectively earthed? What is the resistance from the rope to the mine earth? Is the rope system protected by a LPS? |  |  |
|  | Gag systems |  |  |
|  | Is the foundation connected to the general mass of earth? Is the gag foundation joined to mine earth grid? Is there an LPS protecting the installation site for the gag? Are there earth conductors provided for direct connection to the gag unit? |  |  |
|  | Conveyor counter weight towers |  |  |
|  | Is the foundation connected to the general mass of earth? Is the foundation and structure joined to mine earth grid? Is there an LPS protecting the gravity tower and borehole site? Is there an insulated join between the counterweight tower wire rope and the borehole wire rope? If not, what is the resistance to mine earth? If yes, what is the insulation value of this joint? Wet and dry? |  |  |
|  | Surface fans |  |  |
|  | Do you have surface fans on site? How do you manage the risk of lightning to the surface fan and facility? How do you manage the risk of transferring lightning energy into the underground via the surface fan facility? How do manage the construction of your fan facility to minimise the risks associated with lightning? What is the resistance to mine earth of fan structures? |  |  |
|  | Fuelling facilities |  |  |
|  | Do you have fuelling facilities on site? Do you have a procedure for managing the lightning hazards associated with these fuelling facilities? How do you manage the risk of lightning to the refuelling facilities? How do you manage the risk of transferring lightning energy into the underground via the fuelling facility? What is the resistance to the mine earth of the fuelling facility? |  |  |
|  | Surface infrastructure near boreholes (fences, gas monitoring sheds etc.) |  |  |
|  | Do you have surface infrastructure near boreholes on site? Do you have a procedure for managing the lightning hazards of these surface infrastructures near boreholes? How do you manage the risk of lightning to the surface infrastructure near boreholes? How do you manage the risk of transferring lightning energy into the underground via the surface infrastructure? What method of earthing is used for protecting the surface infrastructure associated with service boreholes? |  |  |
|  | Surface structure near major shafts |  |  |
|  | Do you have surface structures near major shafts on site? Do you have a procedure for managing the lightning hazards of these surface infrastructures near major shafts? How do you manage the risk of lightning to the surface structure near major shafts? How do you manage the risk of transferring lightning energy into the underground via the surface structure near major shafts? What method of earthing is used for protecting the surface infrastructure associated with service boreholes? |  |  |
|  | Power conductor systems (overhead lines and surface and underground cables) |  |  |
|  | Do you have a procedure for managing the lightning hazards of these power conductor systems? How do you manage the risk of lightning to these power conductor systems? How do you manage the risk of transferring lightning energy into the underground via these power conductor systems? What method of earthing is used for protecting the surface infrastructure associated with these power conductor systems What is the resistance from the LPS to the mine earth? |  |  |
|  | Phone and communication systems |  |  |
|  | Do you have a procedure for managing the lightning hazards of these phone and communication systems? How do you manage the risk of lightning to the phone and communication systems? How do you manage the risk of transferring lightning energy into the underground via the phone and communication systems? Is there an LPS to protect these phone and communication systems? What diversion capacity does the LPS system have for the phone and communication systems? Once underground, do you have additional LPS to minimise risk of induction and energy delivery? Are the phone and communication systems suitably shielded from induction from lightning energy? |  |  |
|  | Goafs |  |  |
|  | Do you leave pipelines in active and sealed goafs? Do you leave power cables in active and sealed goafs? Do you leave communication cables in active and sealed goafs? (Phone, DAC, PLC, PED gas monitoring, pull wire and catenaries) Do you leave metallic components in active and sealed goafs? (Screened hydraulic hoses, belt structure) What is your procedure to ensure that lightning energy is not inducted into these components? |  |  |
|  | Redundant metallic equipment and cables |  |  |
|  | Do you have a procedure for managing the lightning hazards of this equipment? How do you manage the risk of lightning to this equipment? How do you manage the risk of transferring lightning energy into the underground via this equipment? |  |  |
|  | Exploration boreholes |  |  |
|  | Do you have exploration boreholes on site? Do you have a procedure for carrying out exploration drilling? How do you manage the risk of lightning to the drilling team and equipment? How do you manage the risk of transferring lightning energy into the underground via the drilling activity? How do you manage the risk of drilling into current or past workings and possible explosive atmospheres? How do manage the construction of your exploration borehole casings to minimise the risks associated with lightning? How do you manage the build up of explosive atmospheres in unused exploration boreholes exposed to lightning? What is the casing resistance to earth? What is the earth resistivity in the area for supplementary earthing of the borehole casing? What is the nominal diameter of these boreholes and does this affect lightning transmission? |  |  |
|  | Gas drainage boreholes |  |  |
|  | Do you have gas drainage boreholes on site? Do you have a procedure for managing the lightning hazards whilst conducting gas drainage? How do you manage the risk of lightning to the gas drainage system and machinery? How do you manage the risk of transferring lightning energy into the underground via the gas drainage activity? How do you manage the risk of drilling into current or past workings and possible explosive atmospheres? How do you manage the construction of your gas drainage borehole casings to minimise the risks associated with lightning? How do you manage the build up of explosive atmospheres in unused gas drainage boreholes exposed to lightning? How do you manage the risk of lightning to the drilling team and equipment? Where your borehole is metal lined, what is the resistance to earth? What is the nominal diameter of these boreholes and does this affect lightning transmission? |  |  |
|  | Service boreholes |  |  |
|  | Do you have service boreholes on site? Do you have a procedure for managing the lightning hazards whilst utilising service boreholes? How do you manage the risk of lightning to the service borehole and installed equipment? How do you manage the risk of transferring lightning energy into the underground via the service boreholes? How do you manage the risk of drilling into current or past workings and possible explosive atmospheres? How do you manage the construction of your service borehole casings to minimise the risks associated with lightning? How do you manage the build up of explosive atmospheres in unused service boreholes exposed to lightning? What method of earthing is used for protecting services that enter the services borehole against lightning? What method of earthing is used for protecting the surface infrastructure associated with service boreholes? Where your borehole is metal lined, what is the resistance to earth? Is the services contained in this borehole bonded to earth and to the borehole? What is the nominal diameter of these boreholes and does this affect lightning transmission? |  |  |
|  | Mine earthing |  |  |
|  | What is the resistance of your mine earthing systems? Are these resistances low enough to dissipate / absorb lightning energies? In high wall entry mines, is the high wall retaining infrastructure suitably earthed? Is equipment in the box cut suitably protected? Is transportable equipment bonded to localised roof and rib mesh to minimise the touch potential due to earth potential rise? Do you have high resistive soils in areas where transportable substations are earthed? Does the design of your mine provide protection for people working underground directly under areas of lightning strikes while in close proximity to earthed machines? |  |  |
|  | High vehicles and transportable equipment |  |  |
|  | Do you control the risk to equipment and personnel? How is this achieved? |  |  |